## Slide 1
ISO 16750-2
ISO 16750-4
ISO 16750-5
TestForge
AI-Powered Automotive Electronics Test Management
✅ 58 backend tests passed
✅ 10 AI backend tests passed
✅ Production build OK
[İsim Soyisim] · EE 471 — Modern Software Development Practices & Technologies · Izmir Institute of Technology
1 / 8

## Slide 2
The Problem
🗂
Manual Test Selection
ISO 16750 test scope determined manually for each DUT. Missed tests, inconsistent coverage across campaigns.
⏱
Repetitive Documentation
Pre-test checklists and formal reports rebuilt from scratch every time, following the same structure.
📂
No Unified View
Results, equipment calibration records, and reports scattered across spreadsheets and local folders.
Automotive ECU validation → 30+ individual tests per DUT · electrical (ISO 16750-2) · climatic (ISO 16750-4) · chemical (ISO 16750-5)
[ DUT REGISTRATION ]
Dolu bir DUT kaydı (mounting location, voltage, temp range)
2 / 8

## Slide 3
System Architecture
Three decoupled services — orchestrated by Docker Compose
Frontend
React 18 + Vite
Tailwind CSS
Chart.js · React Router v6
──────────────
/dut-registration
/test-plan
/checklist
/result-report
/dashboard
/equipment
REST →
Backend API :5000
Flask 3 · Python 3.11
SQLite · 13 tables
Thread-safe DB wrapper
──────────────
/duts /tests /results
/checklists /reports
/equipment /dashboard
/catalog /campaigns
/attachments /export
PDF · DOCX · QR code
HTTP →
AI Backend :5001
Flask microservice
Ollama · Qwen2.5-14B
Local — offline-safe
──────────────
POST /generate-plan
POST /generate-checklist
POST /generate-report
ai_decision_logs table
Structured JSON prompts
Fallback engine
Docker Compose · docker compose up → Frontend :5173 | API :5000 | AI :5001 | SQLite
13 SQLite Tables
duts · tests · results · iso_test_catalog equipment · campaigns · test_plan_items attachments · report_templates · ai_decision_logs
3 / 8

## Slide 4
AI Engine & Evaluation Rules
How test plans are generated and results are evaluated automatically
AI Test Plan Flow
1. DUT params
name · mounting_location · nominal_voltage power_class · temp_min / temp_max · ip_class
↓
2. Catalog lookup
iso_test_catalog → 8 seeded tests applicability_rules_json per DUT profile
↓
3. LLM prompt
Structured JSON prompt → Qwen2.5-14B via Ollama returns: test_name · clause_no · severity · reason
↓
4. Log & store
ai_decision_logs: model_name · prompt · response source (llm / fallback) · status · error_message
⚡ Ollama unreachable → fallback engine activates — full app functionality retained
Evaluation Rules Engine
Per-test JSON evaluation_schema_json — automatic PASS / FAIL
min
field value ≥ threshold
e.g. USmin ≥ 8.0 V
max
field value ≤ threshold
e.g. USmax ≤ 18.0 V
range
min ≤ value ≤ max
e.g. Test Voltage 11–14.5 V
required
field must not be empty
e.g. Chemical Agent required
not_equals
value must not match string
e.g. visual_inspection ≠ 'crack'
Failure → field-level message stored in evaluation_details_json · score in evaluation_score column
4 / 8

## Slide 5
AI Test Plan Generator
▸ DUT parameters → LLM prompt
Mounting location, voltage class, temp range fed into Qwen2.5-14B
▸ ISO 16750 catalog as context
8 seeded tests with applicability_rules_json filter candidate tests
▸ Structured JSON output
test_name · iso_part · clause_no · category · severity · reason
▸ Every decision logged
ai_decision_logs stores prompt, response, model name and source
▸ Fallback-safe
Catalog defaults activate when Ollama is unreachable
[ TEST PLAN PAGE ]
AI tarafından üretilmiş test listesi (ISO madde no, kategori, severity kolonları görünür)
5 / 8

## Slide 6
Result Entry & Automatic Evaluation
▸ Dynamic form from catalog schema
result_input_schema_json drives field type, label, unit, requirement hint
▸ Rules engine evaluates on save
evaluation_schema_json → field-by-field min/max/range checks
▸ PASS / FAIL per field + overall
evaluation_score + evaluation_details_json stored in results table
▸ Deviation tracking
has_deviation → description, root_cause, corrective_action fields
▸ One-click report generation
AI writes formal English report → export as DOCX + PDF with QR code
[ RESULT & REPORT PAGE ]
Ölçüm girişleri + otomatik PASS/FAIL kırmızı/yeşil değerlendirme sonuçları
6 / 8

## Slide 7
Live Demo
▶
VIDEO
~2 min · DUT Registration → AI Test Plan → Checklist → Result + PASS/FAIL → PDF Report → Dashboard
DUT Registration
→
AI Test Plan
→
Checklist
→
Result + Eval
→
Report + Dashboard
7 / 8

## Slide 8
CI/CD Pipeline & Results
GitHub Actions — 4 jobs
git push → trigger
│
flake8 lint (backend + ai_backend)
│
pytest · backend: 58 passed · ai_backend: 10 passed
│
npm lint + test + production build
│
Semantic version bump
feat: → minor · fix: → patch · BREAKING: → major
13
SQLite tables in schema
30+
ISO 16750 tests auto-mapped per DUT
~80%
Less time on report & checklist writing
[ GITHUB ACTIONS ]
4 job — yeşil pipeline (backend · ai · frontend · version)
TestForge: DUT registration → formal test report · zero manual document writing · zero cloud dependency
8 / 8